## Slide 1: Unit 2: Symbol Mapping and TX Filtering
EL-GY 6013: Digital communications
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Describe the steps in symbol mapping and pulse shaping
Describe the common modulation methods:
  BPSK, QPSK, M-QAM.
  For each, compute the minimum distance and symbol energy
Compute the data rate as a function of the modulation and symbol rate
Compute the TX spectrum given pulse shape and DTFT of the symbols
Compute the PSD as a function of the pulse shape and symbol energy
Specify TX filter requirements based on bandwidth and other requirements
Describe the ideal sinc pulse in time domain and frequency domain
Design a digital and analog filter given bandwidth constraints

## Slide 3: This Unit
Channel coding
Symbol mapping
Coded bits
TX filter DAC
IQ symbols
Analog baseband
Upconversion
Info bits
Passband
Channel
Down-conversion
RX filter and ADC
Sync
Equalization
Symbol demod
Channel decoding
RF

## Slide 4: Outline
Symbol mapping
DAC and pulse shaping
Fourier analysis and bandwidth of TX filtering
Power spectral density analysis
Sinc pulse and Ideal low pass filtering
Digitally implementing pulse shaping

## Slide 5: Last Unit: Up- and Down-Conversion
Upconversion in TX: Convert an analog baseband IQ to real passband
Downconversion in RX: Convert real passband to analog IQ
But, baseband signal is complex and analog
How do we transmit digital information?
0
f
f
0
upconversion
downconversion
Analog Baseband
Real passband

## Slide 6: Simple Idea
How do we transmit digital information over an analog channel?
Simple idea: At the transmitter
  Take a sequence of bits e.g.
  Divide time into intervals
  For :
At the receiver:
  Measure in interval
  Determine if or 1
Bits

## Slide 7: Simple Idea: Continued
Simple idea exhibits three key steps:
Step 1. Map bits to symbols:
Step 2. Modulate to a pulse
  for
Step 3. Upconvert
Bits

## Slide 8: Digital Modulation General Procedure
Most communication systems follow the same three steps
  Step 1: Bit to symbol map
  Step 2: Pulse shaping
  Step 3: Upconversion (done in last class)
Bits …101001…
Complex symbols
Discrete-time
Complex baseband
DAC & pulse shaping
Symbol mapping
Real passband
Upconversion
Continuous-time

## Slide 9: Step 1: Symbol Mapping
Generally done in three steps:
  Step 1: Bit to symbol map
  Step 2: Pulse shaping
  Step 3: Upconversion (done in last class)
Bits …101001…
Complex symbols
Discrete-time
Complex baseband
DAC & pulse shaping
Symbol mapping
Real passband
Upconversion
Continuous-time

## Slide 10: Step 1: Bit to Symbol Mapping
= sequence of bits.
= sequence of symbol indices
= sequence of complex symbols
Modulation rate: bits per symbol
Symbol period: One symbol every seconds.
Bit rate of bits per second
T
Ex. with M=4 symbols =2 bits per symbol

## Slide 11: Example: BPSK
1 bit per symbol
Symbol is always real

## Slide 12: Example 2: 4-PAM and QPSK
Two bits per symbol
4-PAM: Symbols are multi-level real.
QPSK: Symbol is complex
  Has I and Q parts
Draw bit to symbol mapping table on board

## Slide 13: Higher-Order Modulation
Constellations go up to 1024 in wireline communications
Wireless is typically limited to 64-QAM (6 bits per symbol)
High order modulation:
  Will see need very low noise to detect high order modulation correctly

## Slide 14: Example Problem
Given bit sequence:
What are the first 3 symbols under the QPSK mapping
Suppose the symbol rate is .
What is the data rate?
00
01
11
10

## Slide 15: Outline
Symbol mapping
DAC and pulse shaping
Fourier analysis and bandwidth of TX filtering
Power spectral density analysis
Sinc pulse and Ideal low pass filtering
Digitally implementing pulse shaping

## Slide 16: Step 2: DAC and Pulse Shaping
Generally done in three steps:
  Step 1: Bit to symbol map
  Step 2: Pulse shaping
  Step 3: Upconversion (done in last class)
Bits …101001…
Complex symbols
Discrete-time
Complex baseband
DAC & pulse shaping
Symbol mapping
Real passband
Upconversion
Continuous-time

## Slide 17: Digital-Analog Conversion (DAC)
Simplest idea for generating baseband signal:
Send during symbol :
Use DAC converter: Sometimes called zero-order-hold
Symbol rate =
For complex symbols, use two DACs (one for I, one for Q)
  Then upconvert in analog
DAC
Symbol period

## Slide 18: Problem with DAC only solution
Benefits of using a DAC for modulation
  Simple to implement
  Easy to detect symbols at receiver (just sample in middle of symbol period)
  Used in many examples: e.g. digital signals in circuits. Modulate bits 0,1 to voltages 0, V
But, problems:
  Signal requires high bandwidth due to fast transitions
  Not acceptable for bandlimited transmissions
DAC

## Slide 19: DAC + Filtering
Solution: Add low-pass filter to DAC output.
Removes high frequency components
Questions:
  Can we still recover from signal ?
  How do we measure the bandwidth of the signal
  What is the effect of the filter on the bandwidth
DAC
Low-pass filter
DAC output before filtering
Filtered signal

## Slide 20: Infinite Pulse Series Representation
Can write DAC output as:
Then filtered output is:
Pulse shape:
DAC
Low-pass filter

## Slide 21: Theoretical Pulse Shape Model
Can model DAC + LPF via filtered pulse train
Real DAC
(ex. Zero-order hold)
Low-pass filter
Physical implementation
Model for analysis
Ideal pulse DAC
Pulse shape filter

## Slide 22: Zero ISI Pulse
Consider linear modulation:
Question: Can we recover from ?
Definition: A pulse is a zero ISI pulse if and for all
  ISI = intersymbol interference
If is a zero ISI then:
Design idea: Find a zero ISI pulse, then recover symbols by sampling

## Slide 23: Simple Pulse Shapes
Pictures on board
Rectangular pulse: Leads to zero-order-hold
Triangular pulse: Leads to linear interpolation
Zero ISI condition

## Slide 24: Sample Problem
Suppose the complex symbols are:
Given pulse as shown to right
Draw the real and imaginary components of
Where would you sample to recover ?
0
T
2T
1

## Slide 25: Outline
Symbol mapping
DAC and pulse shaping
Fourier analysis and bandwidth of TX filtering
Power spectral density analysis
Sinc pulse and Ideal low pass filtering
Digitally implementing pulse shaping

## Slide 26: Bandwidth and US Spectral Allocations

## Slide 27: Bandwidth: A Basic Resource
Limited by:
  Nature of the medium. Most channels can transmit only limited range of frequencies
  Ownership / allocations
We will see that data rate is proportional to bandwidth
  Assuming power per unit bandwidth is constant
Basic questions:
  How do we measure bandwidth?
  What is the bandwidth of linearly modulated signals?

## Slide 28: Fourier Transform of Modulated Signal
Want to measure occupied bandwidth of
Look at FT
Problem: How do we compute FT of ?
Depends on two factors:
  DTFT of
  Pulse shape filter response
Ideal pulse DAC
Pulse shape filter

## Slide 29: Review of DTFT
Given discrete-time sequence
DTFT:
Inverse DTFT:
Note is always a periodic signal
is the discrete frequency. Units is radians per sample.

## Slide 30: Common DTFT Pairs
See Wikipedia

## Slide 31: Fourier Analysis of Modulation
Computing follows three steps:
Compute . This is periodic
Compute
  Vertical scale is unchanged
  Digital frequency mapped to
  This is periodic with period
Compute
Ideal pulse DAC
Pulse shape filter

## Slide 32: Example Problem: Part 1
Given as shown
Suppose
Draw
Solution:
  has period
  Same vertical scale as
  maps to MHz
  maps to MHz
0
0

## Slide 33: Example Problem: Part 2
Suppose filter is:
Draw and
Solution
  Use equation to draw
  Get from
  In this case, filter attenuates two sidelobes
0
0
0.1

## Slide 34: Outline
Symbol mapping
DAC and pulse shaping
Fourier analysis and bandwidth of TX filtering
Power spectral density analysis
Sinc pulse and Ideal low pass filtering
Digitally implementing pulse shaping

## Slide 35: Review: PSD of a Continuous-Time Signal
Let be a power signal
Select frequency to measure PSD
Filter with narrowband filter
  for
Measure power
PSD at is defined as
Can show this is equivalent to window definition
Reveals how much power is in a certain frequency
Narrowband filter around
Power meter

## Slide 36: PSD of a Discrete-Time Signal
Can define PSD of a discrete-time power signal similarly
Let be a discrete-time signal
Select frequency to measure PSD
Filter with narrowband filter
  for
Measure power
PSD at is defined as
Narrowband filter around
Power meter

## Slide 37: Symbol Mean and Energy
Consider a linear modulated signal:
What is its PSD?
Assume . constellation points
Define symbol mean and symbol energy:

## Slide 38: PSD of a Linear Modulated Signal
Suppose: Output of ideal DAC is
After pulse shaping:
Suppose is a discrete-time power signal with digital PSD
Theorem: PSD of and
  Note that is periodic with period .

## Slide 39: Special Case: IID Symbols
Suppose: Output of ideal DAC is
After pulse shaping:
Suppose that:
  Assume are uncorrelated and zero mean
  Average symbol energy:
Then
Power

## Slide 40: Example Problem: Part 1
Given PSD of as shown with
Suppose
Draw PSD of
Solution:
  has period
  Vertical scaled by
  maps to MHz
  maps to MHz
0
0

## Slide 41: Example Problem: Part 2
Now suppose
Draw
Solution:
  Scales low-pass signal by
  Removes all sideloble
Total power in the signal:
  Area of a trapezoid
0
0

## Slide 42: Measuring Bandwidth
PSD of modulated bits is
  Complex baseband signal
  After upconversion will be shifted to
Definition: Signal is exactly band-limited to
  if for
Exact bandwidth =
Approximate BW: Typically require for
Different measures of approximate bandwidth
  3 dB bandwidth
  98% bandwidth, …

## Slide 43: Examples
Recangular pulse:
  99% bandwidth = 10.1/T, 90% BW = 0.85/T
Sinusoidal pulse (for ):
  No discontinuities. Less very high frequency components
  99% bandwidth = 1.2/T

## Slide 44: Spectral Masks
Bandwidths for wireless devices are regulated
  Must transmit most energy in some specified band
  Ensures no interference between channels
Constraints are specified by a spectral mask
  Represents maximum power level in each band
Emissions outside the main band typically very low
  At least 20 to 40 dB below main lobe
Channels for 802.11ad
Each channel is 2.16 GHz

## Slide 45: Signal Bandwidth and Excess Bandwidth
Usually, signal of interest is contained in smaller band
  Signal bandwidth < occupied bandwidth
Excess bandwidth = Occupied – Signal bandwidth
  Allows a transition region
  Filters cannot roll off infinitely fast
802.11ad example:
  Sample rate typically 1.76 Gsamp/s
Lower frequencies, excess bandwidth is even smaller
  Ex. LTE 20 MHz channel
  Signal bandwidth = 18 MHz
  Excess bandwidth
Spectral mask for 802.11ad
Signal bandwidth=1.76 GHz
Occupied bandwidth=2.16 GHz
Excess bandwidth=22%

## Slide 46: Outline
Symbol mapping
DAC and pulse shaping
Fourier analysis and bandwidth of TX filtering
Power spectral density analysis
Sinc pulse and Ideal low pass filtering
Digitally implementing pulse shaping

## Slide 47: Design Goals
Want to design pulse with two goals
Goal 1. Bandwidth limits:
  Most systems (esp. RF) impose bandwidth limits on transmissions.
  PSD of modulated bits is
  Want for where is (single-sided) bandwidth limit
Goal 2: Recover symbols from
  Sufficient condition: Use zero ISI pulse
  Then recover with correct sampling
Can we find a pulse shape satisfying both goals?

## Slide 48: Sinc Pulse
Use sinc pulse
Satisfies zero ISI condition:
  for
Pulse shape frequency response:
  for
Two-sided bandwidth is
Conclusion: sinc pulse satisfies two goals
  If BW limit >

## Slide 49: Sinc Pulse Shaping Illustrated
BPSK symbols
Sinc pulse interpolates the symbols exactly
No out of band emissions
But:
  Waveform varies rapidly between samples
  Synchronization offsets will cause errors
  High peak-to-average ratio
  Needs an infinite length to implement

## Slide 50: Cosine Filtering
Set of filters parametrized by
  is called the rolloff
Excess bandwidth percentage
Ideal sinc filter
  No excess bandwidth.
  Creates excess bandwidth
  But, allows shorter filter

## Slide 51: Cosine Filtering Illustrated
Plotted to the right:
  BPSK symbols filtered with raised cosine filters
Higher values of
  Symbol transitions are faster
  More out-of-band emissions
  But, less peak-to-average
  Less variations between symbols

## Slide 52: Outline
Symbol mapping
DAC and pulse shaping
Fourier analysis and bandwidth of TX filtering
Power spectral density analysis
Sinc pulse and Ideal low pass filtering
Digitally implementing pulse shaping

## Slide 53: Problems with Analog LPF solution
Up to now, we have assumed simple two stage linear modulation
  DAC followed by LPF
Challenges: LPF must be implemented in analog.
  Want LPF filter to approximate ideal Rectangular response
  Difficult to implement in analog
  Analog filters typically have limited roll-off
DAC
Low-pass filter

## Slide 54: Practical Pulse Shaping Block Diagram
Practical pulse shaping:
  Combination of analog and digital filtering
Complex symbols rate =
Digital LPF, cutoff
rate
Upsample by with zero insertion
DAC
Analog LPF, cutoff
Complex baseband

## Slide 55: Practical Pulse Shaping
Start with symbols at
Upsample by with zero insertion
Digitally filter with
Pulse shape with DAC
Analog filter

## Slide 56: Frequency Domain Analysis 1
= DTFT of at symbol rate
Step 1: Upsample with zero insertion:
  Upsampled signal has symbol rate
Step 2: Digital filter with DTFT
  Design filter to have cutoff at
  Theoretically, can use infinite sinc
  But, in practice use long FIR filter

## Slide 57: Frequency Domain Interpretation 2
Step 3: DAC and analog filtering
  Create an impulse train
  Repeated images once every
  Then,
  Cut-off frequency of at
  Removes images

## Slide 58: Images 1
Complex symbols
Upsampling w/ zero insertion ( shown)
Digital filtering
0
0
0
Cutoff=

## Slide 59: Images 2
Pulse train
DAC and analog filtering
0
0
Cutoff=

## Slide 60: Power Spectral Density
Suppose symbols are i.i.d. with
Can show PSD of is:
  Effective pulse shape:

## Slide 61: Effective Pulse Shape
Can show that the resulting signal is
Effective pulse shape is: